## Slide 1
Chessboard Detection
Input Frame
HSV Color Space
The ROI (region of interest) contains the chessboard in the frame.
We store the masks for future use.
For each frame after the initial detection we apply the already stored masks to get the same ROI.
Introduction
Recent technologies e.g., AI pushed robotics field more into the spotlight.
With chess becoming more popular lately, our project aims to elevate the experience through innovative technology.
Integrating the rising popularity of chess with advancements in robotics, our project pioneers an interactive robotic chess experience.
Goals
Building a fully functioning chess game against robotic arm based on,
  Stereo depth camera.
  Physical chess board and pieces.
  Gameplay guided by visual cues, no computer interaction needed.
Identifying player actions.
Detect the chess board in the frame.
Picking and Placing chess pieces with the robot.
Solving incorrect moves.
Pinpointing piece locations for precise robotic arm movement.
A sequence of moves is executed
by the arm
Challenges
Stockfish Engine
Results
Conclusions
Accurate chessboard detection in space and division into 8x8 squares.
Successful game-state detection after each change in the physical chessboard.
Successful and accurate pick and place by the robot even upon initial failures.
Interactive game with varying difficulty levels.
Move Recognition Algorithm
Stockfish is a chess engine designed to analyze and improve players' chess strategies.
  Used to identify the optimal next move in a game.
  checks the legality of moves made by players.
RoboChess: Chess Playing Robotic Arm
Using Image Processing & Computer Vision
Ahmad Ghanayem and Muhammed Ghanayem, Supervised by Elisei Shafer
Motion Detection
    We capture and store the initial depth map at the game's start.
    If the current depth map differs from the initial, we pause the game.
    Players can move pieces by hand, temporarily halting scans until their hand is removed.
Arm Control
Input Frame
Circle Hough transform based solution.
Beginning with the chess starting position, we track every move for interactive gameplay.
Accurate and consistent piece detection.
The arm receives starting and ending squares, then guides its movements precisely.
Using inverse kinematics, we calculate precise joint angles based on desired distances.
If gripping fails, the arm continues searching with varying search radii until success.
When the gripper detects a pressure change, it confirms a successful vacuum grip.
Tesla Optimus Gen 2 AI Humanoid
A fully operational chess game with a robotic arm, including complex moves like castling and en passant.
A user interface accompanies the game for display and control purposes.
The ability to detect illegal moves.
March 2024
Warped Frame
Find ROI
ROI
Warp Frame
Detect Chessboard Corners
Circle Hough on each square
A circle's shift from one square to another indicates movement.
If a circle disappears, it signals a capture, pixel comparison reveals the captured piece.
xArm Lite 6 with no end effector
chess.com puzzles made by stockfish engine
Depth map from from Intel Realsense D435
Inverse kinematics Jacobian matrix
Robotics kinematics model
UI visualizes chess game progress.